## Slide 1
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE
INTELLIGENT TRAFFIC SIGNAL CONTROL
USING FUZZY LOGIC
Adaptive green-light timing with priority-aware scheduling
Python 3 • Tkinter GUI • Fuzzy inference rules
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
1

## Slide 2
Problem Statement & Objectives
Why adaptive traffic signal control?
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
2
Fixed-time signals use predetermined green durations even when traffic varies.
Unequal queues and waiting times can lead to avoidable delays.
Goal: estimate a suitable green duration from vehicle count and waiting time.
Ensure only one direction is green at a time; the other three remain red.
Serve North, South, East, and West once in each scheduling cycle.

## Slide 3
What Is Fuzzy Logic?
Reasoning with degrees of membership rather than strict yes/no categories
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
3
Traditional Boolean logic: true or false.
Fuzzy logic: membership can range from 0 to 1.
0 = no membership; 1 = full membership; values between = partial membership.
A traffic count can partly belong to both “medium” and “high” density.
Membership value
0.0
0.5
1.0
Example:
Medium density = 0.7
High density = 0.2

## Slide 4
System Overview
Fuzzy logic calculates duration; a separate scheduler chooses the next road
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
4
1. Traffic inputs
Vehicle count Waiting time
→
2. Fuzzification
Low / Medium / High Short / Medium / Long
→
3. Rule evaluation
IF–THEN rules AND = minimum
→
4. Green-time output
Weighted average 10–60 seconds
→
5. Scheduler
Longest wait first Vehicle count breaks ties
Inputs → fuzzy inference → suggested duration → priority scheduler → one active green signal

## Slide 5
Inputs & Fuzzy Categories
Each approach is evaluated independently
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
5
INPUT 1: TRAFFIC DENSITY
• Low
• Medium
• High
INPUT 2: WAITING TIME
• Short
• Medium
• Long
Overlapping membership functions allow partial membership in more than one category.

## Slide 6
Fuzzy Rule Base
Nine rules map density and waiting-time categories to green duration
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
6
Density | Short wait | Medium wait | Long wait
Low | 12 s | 18 s | 28 s
Medium | 22 s | 32 s | 42 s
High | 35 s | 45 s | 58 s
Higher density and longer waiting generally lead to longer green durations.

## Slide 7
How Is Green Time Calculated?
Fuzzy AND uses the minimum; active rule outputs are combined by weighted average
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
7
T = Σ (rule strength × rule duration) / Σ rule strengths
Example: Medium density = 1.00, Short wait = 1.00
Rule: IF density is Medium AND wait is Short, THEN green = 22 seconds.
Strength = min(1.00, 1.00) = 1.00.
If this is the only active rule, suggested green time = 22 seconds.
The output is bounded to 10–60 seconds and rounded for the countdown.

## Slide 8
Priority Scheduling
Two different decisions: how long vs. which direction next
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
8
FUZZY CONTROLLER
Calculates green duration
from vehicle count + waiting time
SCHEDULER
Selects the next road:
longest wait first; vehicle count breaks ties
North
Green: calculated
South
Green: calculated
East
Green: calculated
West
Green: calculated
Only one approach is green at a time; the other three remain red.

## Slide 9
Application Workflow
What the user does in the demo
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
9
New Traffic: generates vehicle counts and waiting-time values for all four directions.
Run Fuzzy Controller / Calculate & Start: calculates durations and starts the signal cycle.
Active road turns green; the other three remain red.
Countdown runs; when it reaches zero, the current road turns red and the next eligible road turns green.
Pause and Resume control the simulation timer.
Inspect approach shows memberships, active rules, suggested duration, and signal state.

## Slide 10
Example Output
Illustrative values from the simulation; actual values vary by generated traffic
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
10
Direction | Vehicles | Waiting time | Example green
North | 10 | 13 s | 22 s
South | 8 | 70 s | 45 s
East | 15 | 25 s | 32 s
West | 6 | 45 s | 28 s
Illustration only: the scheduler prioritizes longer waits among roads not yet served in the cycle.

## Slide 11
Testing, Limitations & Future Work
A simulation prototype, not a real traffic controller
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
11
Test: new traffic, start, countdown, pause/resume, inspect each approach, full cycle.
Limitation: traffic and waiting times are simulated.
Waiting time does not automatically increase while waiting.
Membership boundaries and rule outputs are manually chosen.
No pedestrian, emergency-vehicle, or clearance-interval model.
FUTURE ENHANCEMENTS
Increase waiting time dynamically.
Add yellow and all-red clearance phases.
Allow manual editing of inputs and rules.
Compare with fixed-time signals using average delay.

## Slide 12
Conclusion
What this case study demonstrates
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
12
Fuzzy logic handles gradual traffic categories with membership values from 0 to 1.
Nine IF–THEN rules calculate an adaptive green-light duration.
A separate scheduler selects the next direction using waiting-time priority.
The simulation keeps only one direction green at a time and cycles through all four.
The GUI makes the decision process visible and explainable.
Educational demonstration only — not suitable for controlling real traffic infrastructure.

## Slide 13
References
Sources for the concepts and implementation
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE | FUZZY LOGIC TRAFFIC CONTROL
13
L. A. Zadeh, “Fuzzy Sets,” Information and Control, vol. 8, no. 3, pp. 338–353, 1965.
Timothy J. Ross, Fuzzy Logic with Engineering Applications, 3rd ed., Wiley, 2010.
Python Software Foundation, tkinter documentation: docs.python.org/3/library/tkinter.html.
Project implementation: fuzzy_traffic_signal.py.